## Slide 1: NRC’s Integrated Low-Level Radioactive Waste Disposal Rulemaking
DOE Performance And Risk Assessment Community of Practice Webinar
Priya Yadav
David Esh
July 13, 2023

## Slide 2
Rulemaking background
Safety case and technical assessments
Radon and Table Calculator
Timeframes (compliance period)
Waste acceptance
GTCC waste considerations
Exception criteria and significant quantities
Implementation guidance
Schedule and contacts
Agenda

## Slide 3
  LLW Disposal rulemaking to address waste streams that differ significantly in quantity and concentration from what Part 61 originally assumed
    SECY-16-0106 to the Commission as draft final rule
  Regulatory basis for the disposal of Greater-than-Class-C (GTCC) waste through means other than deep geological disposal (SRM-SECY-15-0094)
    In 2019 the NRC issued the draft regulatory basis for public comment
    The regulatory basis concluded that most of the GTCC waste streams are potentially suitable for near-surface disposal
Prior Rulemaking Efforts

## Slide 4
  Combine the Part 61 and GTCC efforts to address overlapping technical requirements, streamline stakeholder outreach, and gain efficiency in proceeding as one rulemaking activity (SECY-20-0098)
  Commission issued Staff Requirements Memorandum (SRM-SECY-20-0098) on April 5, 2022
Commission Directions

## Slide 5
Depleted Uranium
GTCC waste
TRU Waste
Integrated
Low-Level Radioactive Waste Disposal
Rulemaking
Site-Specific Analyses
  Consolidate and integrate criteria for GTCC and 10 CFR Part 61 rulemaking
  Conduct site-specific analyses for all waste streams including DU and GTCC waste
  Include graded approach for compliance period
  Include TRU waste in the definition of LLW
  Address physical protection and criticality concerns in GTCC waste streams
  Provide for Agreement State licensing of certain GTCC waste streams
Integrating the LLW Rulemakings

## Slide 6
Safety Case
Widely recognized internationally
Original Part 61 has many elements
Useful to stakeholders to better understand basis for decisions
Technical Analyses (61.13)
Performance assessment (not new – renamed)
Intruder assessment (new)
Site stability assessment (new for significant quantities of long-lived)
Operational safety assessment (for some types of GTCC waste)
Performance period analyses (for significant quantities of long-lived)
Safety Case and Technical Assessments

## Slide 7
A high-level summary of the information and analyses that support the demonstration that the land disposal facility will be constructed and operated safely – think executive summary.
Provides reasonable assurance that the disposal site will be capable of isolating waste and limiting releases to the environment.
Describes the strength and reliability of the technical analyses.
Safety Case

## Slide 8
Performance Assessment
The technical analyses completed for existing sites for the potential impacts to an offsite member of the public are considered synonymous with a modern performance assessment
Understanding, tools, and capabilities have improved significantly since the early 1980’s
Significant guidance developed to support the proposed requirements for performance assessment (e.g., FEPs, uncertainty, model support)

## Slide 9
Performance Assessment – Guidance Example

## Slide 10
Some regulations have radon flux limits whereas others include radon in dose limits
EPA - 40 CFR 61 in some cases provides radon flux limits (DOE, phosphogypsum stacks, uranium mill tailings disposal) and in others provides standards to include radon as part of public dose limits @ 10 mrem/yr (uranium mines, non-NRC federal facilities)
Cannot resolve the different treatments of radon in regulations in this rulemaking
Can ensure treatment is internally consistent within Part 61 and within NRC in general
Performance Assessment - Radon

## Slide 11
Current Part 61 considered only small quantities of uranium, therefore, radon was not an issue
Existing guidance – include radon (NUREG-1573)
The receptors for different performance objectives (offsite vs. intruder) create practical challenges for application of flux limits
NRC public dose limit (10 CFR Part 20.1301) includes all pathways and all radionuclides.
10 CFR Part 40 (offsite public) and 10 CFR Part 20 subpart E (restricted release) include radon
Performance Assessment - Radon

## Slide 12
Intruder Assessment
The basis for 61.55 in the current regulation is an NRC intruder assessment
Revised requirements would allow for a site-specific intruder assessment
This is a flexible and risk-informed approach

## Slide 13
Intruder Assessment

## Slide 14
TableCalculator
To increase understanding of Part 61 and facilitate commenting on proposed regulations NRC completed the TableCalculator project
The original calculations supporting 61.55 were found in a series of large NUREGs
TableCalculator is a modern tool to increase transparency (available through the NRC RAMP website)
NRC is not changing the 61.55 tables in the integrated rulemaking (will evaluate in future)

## Slide 15
TableCalculator

## Slide 16
Site Stability Assessment
Most problems with early disposal sites arose from short-term stability issues
Those problems were addressed through design and site characteristic requirements
Disposal of significant quantities of long-lived radionuclides may require long-term stability assessment
  Addressed in the context of 61.41 and 61.42

## Slide 17
Operational Safety Assessment
Operational safety (61.43) is typically achieved through a combination of systems, procedures, controls, and training
Accidents scenarios were evaluated by NRC when 10 CFR 61 was developed
Some GTCC waste may contain sufficient radioactivity that an operational safety assessment may be necessary

## Slide 18
Performance Period Analyses
Performance period only applies if significant quantities of long-lived radionuclides will be disposed
Expected proposed standard is to reduce exposures to the extent reasonably achievable
Provide transparency to stakeholders on the expected long-term performance of the disposal system
Long-term results not a measure of projected human health impacts

## Slide 19
Safety and Compliance
Safety can be achieved through different means:
  Disposal concept
  Prescriptive design
  Technical analyses
Proposed approach leans more heavily on technical analyses to afford greater flexibility

## Slide 20
  Commission direction has two options
    Peak dose or
    Use different compliance periods depending on the long-lived component of the waste
  Staff is considering the latter option – flexible and site-specific
  Compliance period of 1,000 years without significant quantities of long-lived radionuclides otherwise 10,000 years and performance period
Timeframes (Compliance Period)

## Slide 21
Timeframes (Compliance Period)
  Carefully examined comments on this issue
  Primary consideration is current practices by Agreement States (AS)
      Compatibility class will likely allow the AS to be more restrictive
  Considered what has been done in the US and internationally

## Slide 22
Timeframes (Compliance Period)
  Uncertainties in societal and environmental conditions will increase over time
  Regulatory approval to allow disposal needs to evaluate impacts, recognizing the uncertainty – not stop the analysis
  Other approaches could be used to mitigate uncertainties:
    Require deep geologic disposal (i.e., Germany)
    Place restrictions on long-lived radionuclides appropriate for near-surface disposal
    Use design requirements (e.g., 10+ m disposal depth for large quantities of depleted uranium)

## Slide 23
Timeframes (Compliance Period)
DRAFT

## Slide 24
Timeframes (Compliance Period)
Class A
DRAFT

## Slide 25
Site-Specific Waste Acceptance Criteria (WAC) (§ 61.58)
Generic: Use §61.55 limits, §61.56
Site-Specific: results of §61.13 technical analyses
Licensees review their waste acceptance program annually
If approved, incorporated into license
Generators still use §61.55 for waste classification
25
Waste Acceptance

## Slide 26
  Near-surface disposal requires 5 m depth and intruder barrier
  10,000 nCi/g threshold
      Case-by-case approval by Commission
  Additional waste characteristics requirements in § 61.56
      Heat generation, radiolysis, criticality
      Not dispersible
GTCC Waste Considerations - Disposal

## Slide 27
  Current requirements under Part 61 require demonstration of criticality safety procedures for preventing criticality accidents without consideration of the concentration of fissile material in the waste (prior to disposal)
      Provide an exemption for radioactive waste with very dilute concentrations of fissile material for which there are no credible means to achieve a critical condition
  Include an additional requirement for disposal units containing significant amounts of fissile material (following disposal)
      Applicant must identify design measures that limit the potential for reconcentration of fissile material
27
GTCC Waste Considerations - Criticality

## Slide 28
Current requirements mandate licensees receiving or possessing nuclear material (SNM) in quantities that exceed the 10 CFR 150.14
  Must satisfy the physical security requirements of 10 CFR 73.67, a “common defense and security” regulation that can only be enforced by the NRC
Provide an exemption in NRC Regulations (10 CFR 73.67) for physical protection of waste at a near-surface disposal facility containing very dilute quantities of SNM
  Physical protection of radioactive waste commensurate with the threat and limited attractiveness
  Physical protection requirements remain under 10 CFR Parts 20 and 37
28
GTCC Waste Considerations – Physical Protection

## Slide 29
§ 61.1 (b) (Purpose and scope)
  Exception criteria
    the land disposal facility license was originally issued before the effective date of this rule; and
    the licensee does not accept a significant quantity of long-lived radionuclides after the effective date of this rule
Licensees who meet these exceptions do not need to comply with revised Technical Analyses (§ 61.13), revised Performance Objectives (§ 61.41 and § 61.42), and WAC (§61.58)
Excepted licensees would be required to comply with original Part 61 regulations
Exception Criteria

## Slide 30
Definition in § 61.2
  Significant quantities of long-lived radionuclides means an amount (volume or mass) and concentration accepted for disposal after the [effective date of this rule] that could, if released, result in the performance objectives of subpart C of this part not being met.
Amount for selection of compliance period (1,000 or 10,000 years)
Amount for demonstrating meeting exception criteria
For the purposes of this paragraph, less than 10 metric tons of depleted uranium is not considered a significant quantity of long-lived radionuclides.
What are Significant Quantities?

## Slide 31
Site-specific calculations to determine what amounts are significant
  Though a simple approach is preferred, to properly account for the multiple key factors a more complex approach could be needed
  Determined by licensee and approved by regulators
Example approaches included in NUREG-2175
  Table of concentrations of long-lived radionuclides for potential use as generic screening values
Significant Quantities

## Slide 32
Draft in NUREG-2175 in 2015 for public comment
Draft final version of guidance published in 2016 on NRC Part 61 website
Updates for Revision 1
  Appendix for GTCC waste disposal considerations
  Appendix for approach to calculate significant quantities of long-lived radionuclides
  Revisions based on proposed rule language
Implementation Guidance

## Slide 33
Develop Proposed Rule that Integrates GTCC and 10 CFR Part 61 Rulemaking
Hold Public Meetings and Comment Period
Submit to Commission for Approval
Develop Final Rule
Revise NUREG-2175 and Develop GTCC Guidance
Hold for Commission Approval of Proposed Rule
Submit to Commission for Final Approval
Publish Proposed Rule
Hold Public Meetings and Comment Period
Issue Final Guidance
Publish Draft Guidance
Develop Final Guidance
May 2024
Publish Final Rule
November 2025
Hold for Commission Approval of Final Rule
5/17/23 Public Meeting
      Onsite meetings at “sited” states and virtual meetings
Rulemaking
Guidance
You are here
Schedule

## Slide 34
George Tartal george.tartal@nrc.gov 301-415-0016 Priya Yadav
priya.yadav@nrc.gov 301-415-6667
David Esh David.Esh@nrc.gov
301-415-6705
Cardelia Maupin cardelia.maupin@nrc.gov 301-415-4127
Contacts