## Slide 1: Presentation Title
Author
University
March 25, 2025
CRESP’s Landfill Partnership and the Performance and Risk Assessment Community of Practice
Craig H. Benson, PhD, PE, NAE
Wisconsin Distinguished Professor Emeritus
University of Wisconsin-Madison
Dean of Engineering Emeritus
University of Virginia
chbenson@chbenson.org

## Slide 2
Strategic Assessment
Education
Review
Applied Research
CRESP Functional Approach
Waste Processing & Special Nuclear Materials
Nuclear Waste Management Policy and Strategy
Stakeholder Engagement and Communication
Remediation, Near Surface Disposal & Long-term Stewardship
Focus Areas
Technically Sound Base to help DOE accomplish environmental management priorities
Certainty
Credibility
Capability
Confidence
in environmental management decisions
CRESP
What is CRESP?
CRESP = Consortium for Risk Evaluation with Stakeholder Participation
Consortium of faculty, research scientists, and students providing research, technology, reviews, strategic assessment and continuing education to support DOE-EM mission
Funded by DOE-EM, but independent and arm’s length.

## Slide 3
What is CRESP’s Landfill Partnership?
Waste
Radon Flux
Water Percolation
Flux to groundwater
Landfill Partnership conducts applied research, assessment, and technology development for on-site disposal facilities and containment systems at DOE facilities:
Understand and predict long-term performance (lab, field, modeling).
Develop and demonstrate sustainable, effective, and economic strategies.
Develop innovative solutions to address difficult problems (Hg, Tc-99).
Provide site-specific problem solving on containment issues.
Hands-on practical technology for disposal facilities.
Notes: SA6-01: Waste Forms and Cementitious Barriers Partnership

## Slide 4
PRACOP and the Landfill Partnership
CRESP’s Landfill Partnership – solves practical issues that address DOE site operations and performances assessments.
PRACOP – forum to discuss and share real-world issues with technology for environmental management and performance assessment.
PRACOP informs CRESP of current and forthcoming questions/issues that can be resolved through applied research.
Notes: SA6-01: Waste Forms and Cementitious Barriers Partnership

## Slide 5: Examples of PRACOP-Informed Activities: Liner Effectiveness for PFAS
PFAS
Sequestration
PFAS to Groundwater
PFAS Concentration in Municipal Solid Waste
Landfill Leachates (Lang et al. 2017)
MCL = 4 ng/L
Can disposal facility contain PFAS?
Are Composite Liners Effective Barriers to PFAS?

## Slide 6: Specific Questions to Answer
Conventional Composite Liner System
Figures courtesy M. Othman, Geosyntec Consultants
Composite liner consists of geomembrane (1.5 mm HDPE) over a 0.6-1.2 m thick compacted clay liner or geosynthetic clay liner (GCL).
Drainage layer can be gravel (more common) or geocomposite drain (GCD).
Do PFAS affect the hydraulic conductivity of clay liners or GCLs?
Do PFAS diffusive readily through geomembranes like some other organic compounds?
Will Subtitle D composite liners protect groundwater given low MCL for PFAS (< 4 ng/L)?

## Slide 7
PFAS and Hydraulic Conductivity of Compacted Clay Liners and GCLs
Influent solutions for single and multi-PFAS tests (yellow diamonds, blue triangle)
Tests with PFAS (y-axis) yield same hydraulic conductivity within testing reproducibility as tests without PFAS (x-axis).
No impact!

## Slide 8
Section 4
Model Predictions: PFAS Concentration at Groundwater Table (Leachate PFOA = 1000 ng/L)
< 0.0028 ng/m2/yr for CCL Composite
< 7.3x10-8 ng/m2/yr for GCL Composite
@100 yr
Avg. PFAS flux with Defect:
GM Defect
Base of liner 3 m above groundwater table (GWT).
Intact geomembrane (GM) or 10 mm diameter hole in GM (upper left of domain)
PFAS concentrations at GWT extremely low below intact GM.
Concentrations at GWT directly below defect =exceed MCL, but limited to small area below defect (about 3 m diameter). Areal PFAS flux VERY small

## Slide 9: Bluewater, NM U mill tailings disposal facility
3,300 acres, main cell: 16 million cubic yards
Barrier Degradation: Rn Barrier Effectiveness
Do radon (Rn) barriers maintain effectiveness in the presence of pedogenic change of barrier layers in covers?

## Slide 10: Radon Fluxes on Rn Barrier Surface – Falls City, Texas
Test Duration: 5 – 20 hours
CRESP/EM, LM, NRC collaborative study.
Rn fluxes still in compliance with emission standard after 20 yr.
20 pCi/m2-s

## Slide 11: Monticello Disposal Facility - Water Balance Cover
3 ha lysimeter
Will the cover control percolation as projected over its service life?

## Slide 12: PRACOP and CRESP Landfill Partnership
PRACOP provides forum to openly discuss uncertainties, challenges, concerns, and successes.
Questions and concerns regarding methodologies and assumptions in PAs drive Landfill Partnership’s applied research agenda.
Ultimate goal and outcome: problem solving, confidence building, and consensus development.
Certainty
Credibility
Capability
Confidence
in environmental management decisions